## Slide 1
DMV THROWERS
YO-YO & SKILL TOY CLUB
Yo-Yo Maintenance Guide
If your yo-yo isn't working right, use this guide first.
dmvthrowers.club · @dmv_throwers · DC · MD · VA

## Slide 2
TROUBLESHOOTING AT A GLANCE
@DMV_THROWERS
dmvthrowers.club
Slipping / unresponsive
WHY
Response pad came out
FIX
Clean with a Q-tip, then replace pad. Available at club, Amazon, or YoYoExpert.
Slipping / unresponsive
WHY
Bearing needs lubrication
FIX
Apply thick yo-yo lube (best), chapstick without water, or a small drop of cooking oil.
Won't sleep (spin)
WHY
String improperly installed
FIX
Remove bearing, clean it, re-install string correctly.
Won't screw together
WHY
Stripped axle — yo-yo was over-tightened
FIX
Try a longer axle. Still loose? Glue the axle into the stripped half.
Won't sleep (spin)
WHY
Axle knot in string
FIX
Take the yo-yo apart, unwrap the string, reseat it. Or replace the string.

## Slide 3
SECTION 1
Response Pads
When your yo-yo slips and stops returning cleanly
DMV THROWERS · @DMV_THROWERS

## Slide 4
RESPONSE PADS — DIAGNOSIS & FIX
@DMV_THROWERS
dmvthrowers.club
WHAT IT LOOKS LIKE
Symptom:
The yo-yo still spins, but it doesn't return with a tug — or it returns inconsistently.
Cause:
The response pad has worn down or popped out of its groove. Response pads create the friction that grips the string on return.
HOW TO FIX IT
Step 1: Unscrew the yo-yo and locate the response groove — the ring inset around the bearing seat.
Step 2: Clean the groove with a Q-tip to remove debris and old adhesive.
Step 3: Press a new response pad into the groove, sticky side down. It should sit flush.
Where to get pads:
Club supply box (ask an organizer) · Amazon · YoYoExpert.com

## Slide 5
SECTION 2
Bearing & Lubrication
Keep your bearing spinning clean and consistent
DMV THROWERS · @DMV_THROWERS

## Slide 6
LUBRICATION — WHAT TO USE AND HOW MUCH
@DMV_THROWERS
dmvthrowers.club
Goal: a tiny amount of lube on the bearing makes it spin responsively and protects it from wear.
BEST
Thick Yo-Yo Lube
Purpose-built — precise applicator, correct viscosity. Available at YoYoTricks.com or YoYoExpert.com. A single drop goes a long way.
OK
Chapstick (no water ingredient)
Works in a pinch. Apply a thin smear to the bearing with a toothpick. Check the ingredients — avoid any with water.
OK
Small drop of cooking oil
Light vegetable or canola oil. Use sparingly — one tiny drop only. Too much makes the bearing sluggish.
CAUTION
Vaseline / petroleum jelly
Works short-term but the bearing will go unresponsive faster than with proper lube. Avoid if you have better options.

## Slide 7
SECTION 3
String
When to replace it and how to install it correctly
DMV THROWERS · @DMV_THROWERS

## Slide 8
WHEN TO REPLACE YOUR STRING
@DMV_THROWERS
dmvthrowers.club
REPLACE IMMEDIATELY IF...
It's visibly fraying
Frayed string weakens quickly and can snap mid-throw.
It's dirty or stiff
Worn string doesn't slide through mounts cleanly and throws off trick timing.
Knot is tight near the bearing
A tight knot at the axle kills spin time. Replace the string — it's not worth fighting.
KNOTS — WHEN TO IGNORE VS. FIX
1–2 loose knots mid-string:
Not a big deal. Try to work them loose while you play or pinch them out before they tighten.
Tight knot near the bearing:
This will significantly hurt spin time. Replace the string.
Need string?
Bring it up at a meetup — the club keeps string on hand. String is also cheap in bulk online (Amazon, YoYoExpert).

## Slide 9
HOW TO INSTALL A STRING
@DMV_THROWERS
dmvthrowers.club
STEP-BY-STEP INSTALLATION
1
Unscrew the yo-yo
Hold one half in each hand and twist counterclockwise to separate.
2
Open the string loop
Untwist the bottom of the string until you have an open loop about 1 inch wide.
3
Seat the loop on the axle
Slide the open loop around the axle. It should hang loose — this lets the yo-yo spin freely.
4
Screw the yo-yo back together
Tighten until snug. Do not over-tighten — stop as soon as it's firm. Over-tightening strips the axle.
5
Make the slipknot
At the other end, form a slipknot and place it on your middle finger between the first and second knuckle.
6
Check string direction
Throw a sleeper. The string should feed off the top of the yo-yo. If it feeds from the bottom, flip the yo-yo over.

## Slide 10
TYING THE SLIPKNOT
@DMV_THROWERS
dmvthrowers.club
The slipknot is the loop that goes around your finger. It should slide easily — not lock tight.
Position: Seat the loop between the first and second knuckle of your middle finger. This is the safest position and gives the best throw angle.
This is the only 'wrong' way to yo-yo: not wearing the slipknot. Always have the string secured to your finger before throwing.
SLIPKNOT STEPS
1
Form a loop at the string end
2
Cross the loop over itself
3
Pull the tail up through the crossing
4
Tighten to form a fixed loop
5
Size loop to fit your finger loosely
6
Place between 1st and 2nd knuckle

## Slide 11
SECTION 4
Structural Problems
Axle damage, stripped threads, and yo-yos that won't screw together
DMV THROWERS · @DMV_THROWERS

## Slide 12
STRIPPED AXLE & ASSEMBLY PROBLEMS
@DMV_THROWERS
dmvthrowers.club
Problem: Yo-yo won't screw together — threads feel stripped
Cause: The axle has been over-tightened. Screwing the yo-yo too tight strips the threaded insert, making it impossible to reassemble correctly.
Fix Option 1: Try a longer axle — sometimes a slightly longer axle will catch undamaged threads.
Fix Option 2: Glue the axle into the stripped half, or have the threads re-tapped.
Prevention: Tighten the yo-yo until it's just snug — never force it. The yo-yo only needs to stay closed, not locked tight.
Problem: String tangled around the axle (axle knot)
Cause: The string looped around the axle during play instead of sitting loosely in the gap.
Fix: Unscrew the yo-yo, carefully unwrap the string from the axle, then re-install the string correctly. If the string is badly kinked, replace it.

## Slide 13
COMMON QUESTIONS
@DMV_THROWERS
dmvthrowers.club
Q: My yo-yo isn't working right — where do I start?
A: Work through this guide in order: check the response pads, then the bearing lube, then the string. Most problems fall into one of those three categories.
Q: There's a knot in the middle of my string — now what?
A: Try to work it loose before it tightens. 1–2 small knots mid-string aren't a big deal and you can keep playing. A tight knot at the bearing seat means it's time for a new string.
Q: Why can't I land this trick — is my yo-yo broken?
A: Probably not. Some tricks are easier if you've built up the preceding skills first. If it feels mechanical (the yo-yo isn't spinning long enough), check your lube and response pads.
Q: Is there a wrong way to yo-yo?
A: One: not wearing the slipknot. Always have the string secured to your finger before throwing. Everything else is fair game as long as you're keeping the space safe for others.

## Slide 14
DMV THROWERS
YO-YO & SKILL TOY CLUB
Still stuck? Bring it to a meetup.
We keep spare strings, response pads, and lube on hand.
Someone at the club can help you get back to throwing.
Every 3rd Sunday · 1–4 PM · Arlington Central Library
1015 N Quincy St · Arlington, VA 22201
dmvthrowers.club · @dmv_throwers · ko.fi/dmvthrowers